## Slide 1: Advance Modelling for Operations
Group 1

## Slide 2
Weaknesses
5. Class Train:
1. __init__
The position of the tuggers at the beginning of the simulation cannot be equal…tuggers cannot lay on each other. Could influence the consumption the day after, for instance. That is why it should be considered, for both modelling purposes and reality issues.
Next stop If we take into account acceleration and deceleration, if no loads in the next stop have to be charged there is no point in stopping there (saving time, energy, etc.). Thus it is not mandatory to stop at line 1 everytime
2. check_charge: “NA” [Domanda: Non ha senso che la selezioni randomly…]
3. move
“if self.model.schedule_lines.agents[self.next_line].UL_in_buffer >= 1” is wrong. It does not take into consideration the possibility of the lines to create a new UL.
Self.load < self.capacity -> It does not take into consideration the loading’s limit of the tugger. ULs weights differ!
self.remaining_energy -= compute_energy(loading_time) -> Energy consumption depends on the activity (loading in this case) and not solely on time.
self.load += 1 -> Why can’t the tugger take on more ULs than one if it has space?
4.charging:
Do batteries charge linearly? No, charging time depends on battery load.
5.step:
Modelsystem is in integers whereas tasktime is in floats…we are loosing time.
6. ChargingStation:
a) Need to convert the steps in a smaller time unit to avoid loss
6. General: MOVEMENT IS INSTANTANEOUS? CAN WE ACHIEVE A CONTINUOUS MOVEMENT ON THE GRID?
Additional Comments:
Change time-formatting (in minutes)
Between station 3 and 4, the tugger “steals” 10 meters (it gets back, rather than going forward to 75): SOLVED
The tugger does not move, it says fixed at the 1st station, i.e., station[0].: SOLVED
Constant speed
Average speed meant to account for high-speed travel, low-speed turns, and acceleration/ deceleration times.
Battery size
Battery size decreases throughout time depending on the usage.
Compute time
Random.uniform(0,1) is added independently of the distance travelled while it depends on the path the tugger has to do.
Compute energy
Energy does not depend solely on time but also on other variables such as loading weight or speed (acceleration, deceleration)
Class train
Random.uniform(0,1) is added independently of the distance travelled while it depends on the path the tugger has to do.
Code refactoring
Energy does not depend solely on time but also on other variables such as loading weight or speed (acceleration, deceleration)
01
02
03
04
05
06
Errori di modello:
Errori di implementazione: